Green's function in circular geometry
G(x,y,x_0,y_0)= {1} over { 2 %pi %epsilon_0} ln ({bar{R} r_0} over {R a_{0}}) = {1} over { 4 %pi %epsilon_0} ln ({bar{R^2} r_0^2} over {R^2 a_{0}^2})
One:
bar{R}^2 = { {r_0^4 x^2+(r_0^2 y - a_0^2 y_0)^2} over {r_{0}^4} } = { {y_0^4 x^2+r_0^4 y^2 - 2 a_0^2 y_0^2 y_0 y + a_0^4 y_0^2} over {y_{0}^4} } newline {} approx {a_0^4} over {y_{0}^2}
Two:
R^2=x^2+y^2-2 y y_0
Three:
r_0^2=y_0^2

G(x,y,x_0,y_0) approx {1} over { 4 %pi %epsilon_0} ln ({a_0^2} over {(x^2+y^2-2 y y_0)}) = {1} over {4 %pi %epsilon_0} left ( ln ({a_0^2} over {(x^2+y^2)}) + ln (1+{2 y y_0} over {x^2+y^2}) right ) = {} newline {} approx {1} over {4 %pi %epsilon_0} left ( ln ({a_0^2} over {(x^2+y^2)}) +{2 y y_0} over {x^2+y^2} right )
Derivative of G for y if lambda_i
E_{y}(x,y)={1} over {2 %pi %epsilon_0} left ( {y} over {R^2}+ {y_0 (y^2-x^2)} over {R^4} right )
E_{x}(x,y)={1} over {2 %pi %epsilon_0} left ( {x} over {R^2}+ {2 y_0 y x} over {R^4} right )
The kick is proportional to:
%DELTA p prop {1} over {R} left ( 1+{y y_0} over {R^2} right )
The energy is proportional to:
E_kin(y) prop {1} over {R^2} left ( 1+{2 y y_0} over {R^2} right )
If the radius of a pipe in the LHC is around ~2 cm and the beam is offcentered for 1 mm then electrons at the wall above the pipe will get 10% higher energy. Electrons below the beam will get 10% lower energy. If we are at the slope of the SEY curve then more electrons will be produced below the bunch than above. If we are exactly at maximum, then more electrons will be produced to the left and to the right of the beam.
∆